## Slide 1: FPGA Accelerated Ray Tracing
Justin Gallagher
May 8, 2016

## Slide 2: Summary
I implemented a parallel ray tracer, using FPGA hardware to accelerate computation.
  The ray tracer supports CPU operation, multithreading, and SIMD as well, for comparison
This method is very competitive for large payloads, and offers improvements on energy efficiency
  Memory bandwidth limits the performance gain, but this problem can be fixed

## Slide 3: What is Ray Tracing?
Ray Tracing is a image rendering technique that simulates the travel of light through an image.
Photo Credit: Mimigu, Creative Commons Attribution License 3.0
Notes: Allows effects to be easily simulated with little programmatic effort:
Soft Shadows
Reflections
Refraction

## Slide 4: Demonstration
We trace light backwards from each pixel through the scene
Subject
Light source
Ray
Notes: Here, we create a ray extending out from the viewer.
Test it for intersections with the scene’s objects (in our case, triangles).
Trace a path from collisions to light
If material is reflective/refractive, create a new ray travelling in the appropriate direction
Note that this method is highly parallel -> each ray/tri independent
My idea: use FPGA to encode many circuits that can do this calculation – more than we have in cores!

## Slide 5: Hardware & Tools
Xilinx Zynq-7000 System on Chip (“Zedboard”)
  Dual-core ARM Cortex-A9 CPU (@667 MHz) with ARM NEON SIMD
  1GB on board RAM
  On board FPGA in communication with the ARM processor at 266 Mb/s through Direct Memory Access
Xilinx Vivado High Level Synthesis (HLS)
  Interface for compiling C-like code to hardware that can be implemented in the FPGA
C++ Ray Tracer running on ARM
  Heavily based on the 15-462 Computer Graphics ray tracer
  Processes each ray independently, calculating its intersection with triangles in the scene in sequence
  Support for SIMD and FPGA acceleration was added

## Slide 6: The Triangle/Ray intersection algorithm
Each block dependent on the last
This division takes more than 1/3 of the processing time!
Also known as the “Möller-Trumbore” algorithm
Trivial to implement with SIMD – just vectorize the inputs and the operations
Notes: Inherent sequential operation makes this algorithm hard to parallelize internally

## Slide 7: FPGA Parallelism
Problem: The streaming interconnect I use only allows one data read and write at a time
Solution: Create multiple circuits, and stagger their operation so many are calculating while the next is reading and the last is writing
Question: How many circuits should I make?
read | read | read | calc | calc | calc | calc
write | write | write | read | read | read | calc
calc | calc | calc | write | write | write | read

## Slide 8: Memory Limitations
Turns out, 16-20 simultaneous intersections is the best we can do
Chart: More Simultaneous FPGA Intersections: Throughput Approaches Memory Bandwidth
| 1 | 2 | 4 | 8 | 12 | 16 | 20
 | 1033801.9743 | 1795324.6753 | 2376891.3343 | 3217877.095 | 3649419.2186 | 3909502.2624 | 4080283.353
Theoretical Maximum | 4430000 | 4430000 | 4430000 | 4430000 | 4430000 | 4430000 | 4430000 | 4430000
Notes: More than that, and you’re using valuable power + board space for diminishing returns

## Slide 9: Testing Configurations
CPU
  Single-threaded CPU implementation
CPUx4
  4-threaded CPU implementation, running on the dual-core processor
CPU SIMD
  Single-threaded CPU with SIMD vector operations
CPUx4 SIMD
  4-threaded CPU implementation with SIMD vector operations
FPGA
  Single CPU thread sends data to FPGA, which implements 20 simultaneous triangle intersection tests

## Slide 10: Four Testing Scenes
Triangle (1 triangle)
Cubes (34 triangles)

## Slide 11: Four Testing Scenes
Small plane (1084 Triangles)
Large plane (138K Triangles)

## Slide 12: Questions to Ask
  Is the FPGA implementation competitive with the others in terms of throughput?
    What about in terms of energy efficiency?
  What workloads are best suited to each implementation?

## Slide 13: FPGA Becomes More Competitive with Scale
Chart: Scene
| Triangle (1) | Cubes (34) | Small Plane (1084) | Large Plane (138K)
CPU | 528837 | 2641392.2764 | 2690848.5397 | 2690848.5397
CPU SIMD | 424168 | 3567683.9237 | 3631961.7893 | 3923189.7893
CPUx4 | 2013820 | 10459959.7586 | 10978526.3297 | 11358914.3297
CPUx4 SIMD | 1651160 | 14230724.6377 | 14681076.3747 | 14681076.3747
FPGA | 6825 | 194667 | 636760.2265 | 4080283.353

## Slide 14: FPGA is Competitive when Adjusted for Clock Speeds
Chart: Scene
| Triangle (1) | Cubes (34) | Plane (1084) | Large Plane (138K)
CPU | 0.0039601 | 0.0040343 | 0.0040343
CPU SIMD | 0.00063593 | 0.0053489 | 0.0054452 | 0.0058818
CPUx4 | 0.0030192 | 0.015682 | 0.01646 | 0.01703
CPUx4 SIMD | 0.0024755 | 0.021335 | 0.022011 | 0.022011
FPGA | 6.825e-05 | 0.0019467 | 0.0063676 | 0.040803
Notes: FPGA is significantly slower: 100 MHz vs 667 MHz
FPGA requires only half as many clock steps!

## Slide 15: FPGA is More Power Efficient With High Loads
Chart: Scene
| Triangle (1) | Cubes (34) | Small Plane (1084) | Large Plane (138K)
CPU | 344743.807 | 1721898.4853 | 1754138.5526 | 1754138.5526
CPU SIMD | 276511.0821 | 2325739.1941 | 2367641.3229 | 2557490.0843
CPUx4 | 1312790.0913 | 6818748.2129 | 7156796.8251 | 7404768.1419
CPUx4 SIMD | 1076375.4889 | 9276873.9489 | 9570453.96 | 9570453.96
FPGA | 17062.5 | 486667.5 | 1591900.5661 | 10200708.3825

## Slide 16: Conclusion
FPGAs are well suited for very high loads with little synchronization requirements
  Communication overhead becomes irrelevant
  Natural parallelism makes FPGAs extremely flexible, once the programmer overcomes the learning curve
FPGAs can be used to compute simple operations with high energy efficiency
Memory bandwidth is key – and a detail I should have paid attention to earlier

## Slide 17: Future Work
Overcome the memory bandwidth barrier
  Non-stream based memory interfaces
  Reduce the amount of data that needs to be communicated between the FPGA and the processor
Take advantage of parallelism beyond the ray/triangle-level
  “Bundle” data transfers to the FPGA to reduce communication overhead
  Offload color calculations to the FPGA as well
  Perform the “reduce step” on the FPGA, finding the closest triangle intersection rather than the time

## Slide 18: Acknowledgements
Brandon Perez
  Wrote the AXI Direct Memory Access driver for the Zedboard
  Advice and support working with FPGAs
Prof. James Hoe
  Provided Zedboard hardware, software and reading material
15-462 Course Staff
  Built the core of the CPU ray tracer this project is based on
Prof. Kayvon, Prof. Bryant and the 15-418 Course Staff
  Thank you for running a great course!

## Slide 19: Questions
Thank yoU!